## Slide 1
MAY 2019
EFFICIENT DATA PARTITIONING FOR NEURAL NETWORKS
SaURABH GUPTA, AJAY KRISHNA ANANDA KUMAR, RESHMA RAJARAMA NAYAK

## Slide 2: Deep Neural Networks is ubiquitous!

## Slide 3: Deep Learning – Active Research area
Graph source : Dean, Jeff, David Patterson, and Cliff Young. "A new golden age in computer architecture: Empowering the machine-learning revolution." IEEE Micro 38.2 (2018): 21-29.

## Slide 4: Neural network
Driving factors for neural network optimization:
  Large models
  Huge data processing
Key efficiency metrics:
  Compute:
    Parallelization to achieve efficient performance gain
  Memory:
    Reduce communication and synchronization overhead

## Slide 5: Training vs Inference
Training is more challenging
  Roughly 3 times more computations
  Increased storage requirements
  Large DNN models and Datasets
Image Source: https://blogs.nvidia.com/blog/2016/08/22/difference-deep-learning-training-inference-ai/

## Slide 6: Partitioning - Data and Model parallelism
Data parallelism
  Each sample is independent (S).
  Divide image samples among the processing units.
Model parallelism
  Each output channel is independent (M).
  Divide CNN model (weights) among the processing units.

## Slide 7: Convolutional Neural Networks
Input feature map: H*W*N
Output feature map: H*W*M
Weight parameters: K2*N
Number of computations:
H*W*N*K2*M
For K=5, H=W=32*32, N=128, M=128
We need 80*106 operations
Basic Convolution block

## Slide 8: A typical Convolutional Network
There are ~10s-100s of these convolutional block

## Slide 9: Implementation
CUDA primitives developed
  Supports data and model parallelism flavors for Convolutional, average and max pooling, fully connected layers
  Chooses configurations for kernel launch based on the tensors dimensions and batch size
  Supports logistic and RELU activations

## Slide 10: Implementation
Developed three CNN architectures : Lenet-5, AlexNet, ResNet-18
CUDA kernel for fused Convolutional layer : forward and backward input gradient propagation supporting different data layout.
Explored three different GPU architectures and their performance implications
Multi-GPU implementation of AlexNet and communication overhead analysis on 2 and 4 GPUs

## Slide 11: Machine configurations
Property | Tesla K40s | GeForce GTX 1080 Ti | Tesla P100-PCIE-16GB
CUDA Compute capability | 3.5 | 6.1 | 6
Number of SMs | 15 | 28 | 56
Total amount of global memory | 11440 MBytes | 11178 MBytes | 16281 Mbytes
CUDA Cores | 2880 CUDA Cores | 3584 CUDA Cores | 3584 CUDA Cores
GPU Max Clock rate | 745 MHz (0.75 GHz) | 1582 MHz (1.58 GHz) | 1329 MHz (1.33 GHz)
Memory Clock rate | 3004 Mhz | 5505 Mhz | 715 Mhz
Memory Bus Width | 384-bit | 352-bit | 4096-bit
L2 Cache Size | 1572864 bytes | 2883584 bytes | 4194304 bytes
Total amount of shared memory per block | 49152 bytes | 49152 bytes | 49152 bytes

## Slide 12: CNN architectures
Neural Network Architecture | Number of Params | Number of computation (FLOPs)
Lenet-5 | 60840 | 3.41x105
AlexNet* | 28567498 | 1.08x108
Resnet-18* | 10862986 | 1.13x107
Parameters and computation comparisons:

## Slide 13: CNN - Parameters
Input feature map: Inp[N][C][H][W]
Output feature map: Out[N][M][H’][W’]
Kernel Map: Wi[M][C][K][K]
Where:
‘N’ is the batch size
‘C’ and ‘M’ are number of input and output channels respectively.
‘H’ and ‘W’ are input feature dimension
H’ and W’ are output feature dimension (depending on ‘K’, stride and padding)

## Slide 14: RESULTS

## Slide 15: Data Parallel
Occupy GPU by providing more training samples (batch).
Different SMs work on different samples.
Pros:
  More work for GPU to occupy it’s resources.
Cons:
  Higher memory footprint.
Chart: Execution Time vs Batch size
| 1 | 8 | 16 | 32 | 64 | 128 | 256
K40 - Data parallel | 23358.5585 | 12792.0192 | 7295.6648 | 4979.6357 | 4205.0189 | 4645.5684

## Slide 16: Data Parallel – uArch considerations
Chart: Forward Convolution execution time
| 4 | 8 | 16 | 32 | 64 | 128
K40 | 26.5102 | 26.6487 | 27.5827 | 29.7612 | 35.3858 | 43.414
GTX 1080Ti | 9.7335 | 9.6798 | 9.7386 | 10.512 | 12.162 | 15.125
P100 | 12.6485 | 12.5821 | 12.5273 | 12.5086 | 17.7608 | 24.078
Used K40, GTX 1080Ti and P100 GPUs.
K40 gets occupied only after batch size of 16, whereas 1080 Ti & P100 take 32 and 64 batch size respectively.
Even further batch size required to hide the latency

## Slide 17: Model Parallel
Different SMs work on different channel.
Pros:
  Smaller weight matrix can be stored locally in shared memory.
  Reduced global memory traffic.
Cons:
  Unable to fully occupy GPU.
  Defined by DNN architecture, not configurable.
Chart: Memory accesses - Model vs Data
| Shared memory | L1 | L2 | Device
Model | 282624 | 406528 | 1143808 | 11608
Data | 0 | 652288 | 1389568 | 188021.5312

## Slide 18: Model Parallel - Comparison
Performance falls short of data parallel approach when the data parallel batch size is increased.
Explanation: The data parallel execution time decreases sub-linearly with batch size.
Chart: K40 - Execution Time vs Batch size
| 1 | 8 | 16 | 32 | 64 | 128 | 256
K40 - Data parallel | 23358.5585 | 12792.0192 | 7295.6648 | 4979.6357 | 4205.0189 | 4645.5684
K40 - Hybrid | 5523.1772 | 4649.8096 | 4574.9562 | 4548.3135 | 4526.4922 | 4515.7763 | 4516.301
K40 - Model Parallel | 5523.1772 | 5523.1772 | 5523.1772 | 5523.1772 | 5523.1772 | 5523.1772 | 5523.1772

## Slide 19: Model Parallel - Comparison
Chart: GTX 1080Ti
| 1 | 8 | 16 | 32 | 64 | 128 | 256
GTX 1080Ti - Hybrid | 1644.6936 | 1188.9686 | 1178.4478 | 1175.665 | 1166.0499 | 1166.0025 | 1169.9055
GTX 1080Ti - Model Parallel | 1644.6936 | 1644.6936 | 1644.6936 | 1644.6936 | 1644.6936 | 1644.6936 | 1644.6936
GTX 1080Ti - Data Parallel | 7736.8281 | 3931.4909 | 2246.3102 | 1397.4957 | 1312.2564 | 1405.7955
Chart: K40
| 1 | 8 | 16 | 32 | 64 | 128 | 256
K40 - Data parallel | 23358.5585 | 12792.0192 | 7295.6648 | 4979.6357 | 4205.0189 | 4645.5684
K40 - Hybrid | 5523.1772 | 4649.8096 | 4574.9562 | 4548.3135 | 4526.4922 | 4515.7763 | 4516.301
K40 - Model Parallel | 5523.1772 | 5523.1772 | 5523.1772 | 5523.1772 | 5523.1772 | 5523.1772 | 5523.1772
Chart: P100
| 1 | 8 | 16 | 32 | 64 | 128 | 256
P100 - Data parallel | 8719.3791 | 4357.3731 | 2239.5775 | 1275.9072 | 815.7135 | 729.1049
P100 - Hybrid | 1127.7993 | 597.7753 | 596.151 | 588.5545 | 587.5507 | 589.6467 | 595.9165
P100 - Model Parallel | 1127.7993 | 1127.7993 | 1127.7993 | 1127.7993 | 1127.7993 | 1127.7993 | 1127.7993
Execution Time vs Batch size studied on 3 different GPU architectures

## Slide 20: Model Parallel – uArch considerations
See similar trends as Data parallel approach.
Significant number of channels required to occupy the GPU.
Chart: Forward Convolution execution time
| 4 | 8 | 16 | 32 | 64 | 128
 | 0.35946 | 0.36387 | 0.45987 | 0.79683 | 1.265 | 2.2707
GTX 1080Ti | 0.16618 | 0.16628 | 0.16871 | 0.27643 | 0.45922 | 0.72406
P100 | 0.33808 | 0.33821 | 0.33817 | 0.33053 | 0.64556 | 0.96694

## Slide 21: Hybrid Approach
Divide both batch size and number of output channels.
Takes advantage of data locality of model parallelism and sub-linear scaling of data parallelism with batch size.
Saturates with much smaller batch size. Thus, lesser memory footprint.
Chart: K40 - Execution Time vs Batch size
| 1 | 8 | 16 | 32 | 64 | 128 | 256
K40 - Data parallel | 23358.5585 | 12792.0192 | 7295.6648 | 4979.6357 | 4205.0189 | 4645.5684
K40 - Hybrid | 5523.1772 | 4649.8096 | 4574.9562 | 4548.3135 | 4526.4922 | 4515.7763 | 4516.301
K40 - Model Parallel | 5523.1772 | 5523.1772 | 5523.1772 | 5523.1772 | 5523.1772 | 5523.1772 | 5523.1772

## Slide 22: Hybrid Approach
Chart: Execution Time vs Batch size
| 1 | 8 | 16 | 32 | 64 | 128 | 256
K40 - Data parallel | 23358.5585 | 12792.0192 | 7295.6648 | 4979.6357 | 4205.0189 | 4645.5684
K40 - Hybrid | 5523.1772 | 4649.8096 | 4574.9562 | 4548.3135 | 4526.4922 | 4515.7763 | 4516.301
K40 - Model Parallel | 5523.1772 | 5523.1772 | 5523.1772 | 5523.1772 | 5523.1772 | 5523.1772 | 5523.1772
GTX 1080Ti and P100 show similar trend.
K40 and GTX reach data parallel saturation at batch size of 64 but P100 reaches saturation at 128.
Irrespective of DNN and underlying machine architecture, hybrid approach performs better.
Chart: Execution Time vs Batch size
| 1 | 8 | 16 | 32 | 64 | 128 | 256
GTX 1080Ti - Hybrid | 1644.6936 | 1188.9686 | 1178.4478 | 1175.665 | 1166.0499 | 1166.0025 | 1169.9055
GTX 1080Ti - Model Parallel | 1644.6936 | 1644.6936 | 1644.6936 | 1644.6936 | 1644.6936 | 1644.6936 | 1644.6936
GTX 1080Ti - Data Parallel | 7736.8281 | 3931.4909 | 2246.3102 | 1397.4957 | 1312.2564 | 1405.7955
Chart: Execution Time vs Batch size
| 1 | 8 | 16 | 32 | 64 | 128 | 256
P100 - Data parallel | 8719.3791 | 4357.3731 | 2239.5775 | 1275.9072 | 815.7135 | 729.1049
P100 - Hybrid | 1127.7993 | 597.7753 | 596.151 | 588.5545 | 587.5507 | 589.6467 | 595.9165
P100 - Model Parallel | 1127.7993 | 1127.7993 | 1127.7993 | 1127.7993 | 1127.7993 | 1127.7993 | 1127.7993

## Slide 23: Comparison of schemes for other networks
Chart: Lenet-5
| 1 | 8 | 16 | 32 | 64 | 128 | 256
Data Parallel | 39.0919 | 24.7367 | 15.4828 | 9.9065 | 9.0486 | 7.0943
Hybrid | 29.205 | 9.1229 | 7.3281 | 6.6813 | 6.0683 | 5.8101 | 5.5656
Model parallel | 29.205 | 29.205 | 29.205 | 29.205 | 29.205 | 29.205 | 29.205
Chart: ResNet18
| 8 | 16 | 32 | 64 | 128
Data parallel | 959.7842 | 505.4672 | 278.9034 | 172.3239 | 160.4075
Model parallel | 239.724 | 239.724 | 239.724 | 239.724 | 239.724
Hybrid | 150.5463 | 143.2168 | 139.8417 | 136.459 | 134.805
The crossover point of AlexNet and Resnet is around 64 batch size, but Lenet has early crossover, due to the dimensional channels of the former CNN architectures.

## Slide 24: Layer Fusion
Even with above optimizations, each layer has to store data and next layer has to load it back.
We can further reduce memory dependency by storing intermediate results locally.
Possible by partitioning input feature space.

## Slide 25: Layer Fusion
Even with above optimizations, each layer has to store data and next layer has to load it back.
We can further reduce memory dependency by storing intermediate results locally.
Possible by partitioning input feature space.

## Slide 26: Layer Fusion
A bigger tile in Layer 1 serves a smaller tile in Layer 2 to produce a smaller tile of output feature.
Cause re-computations due to tile overlap
Constraints:
  Intermediate tile should be small enough to fit in shared memory.
  Data locality befit should outweigh the amount of re-computations.

## Slide 27: Layer Fusion
Counter intuitively, the execution time increase with the fused implementation.
Explanation: Tiling looses the spatial locality in the input feature space.
Thus, even the layer 1 computation time increases by ~6x.
Chart: Fused vs non-fused implementation
Layer 1 | 1.34 | 6.36
Layer 2 | 1.34 | 2.85

## Slide 28: Layer Fusion – Memory dependency
The compute utilization is pretty low for the fused implementation
Regular
Fused

## Slide 29: Layer Fusion
The memory dependency causes a significant stall in the progress. (~27%).
Effective memory bandwidth too reduces from 340 GB/s in regular approach to 260 GB/s in fused approach.

## Slide 30: Layer Fusion – Move to NHWC
In regular approach, the input feature map is stored as ‘NCHW’.
Since image dimension (‘H’ & ‘W’) are the lower dimensions, tiling causes this dimension to shrink.
NHWC approach on the other hand changes the lowest dimension as number of channels.
With minor changes in computation pattern, this storage enhances coalesced accesses.

## Slide 31: Layer Fusion - NHWC
Obtain much superior results with ‘NHWC’ based feature storage over the ‘NCHW’ storage.
Achieve ~2x speedup of second layer over the non-fused version and achieves ~15% speedup overall.
Chart: Fused NHWC vs non-fused approach - K40
| W/O Fusion | With Fusion
Layer 1 | 1.34 | 1.58
Layer 2 | 1.34 | 0.62

## Slide 32: Layer Fusion - NHWC
The memory dependency with NHWC approach is reduced to <5%.
Effective memory bandwidth increased from 340 GB/s in regular approach to 729.448 GB/s (>~2x) with this NHWC fusion approach.

## Slide 33: Layer Fusion – GTX 1080 Ti
On GTX, the fused layer achieves ~5x speed up over first layer and ~35% speed up overall.
The layer 1 compute time is still higher due to the re-computations in fused implementation.
Chart: Fused vs Non-fused implementation - GTX
| W/O Fusion | With Fusion
Layer 1 | 720 | 872
Layer 2 | 720 | 189

## Slide 34: Layer Fusion – Analytical Model
We developed an analytical model to calculate additional computations and when this tile based approach is effective.
Say, we have ‘SHRD’ amount of shared memory.
Intermediate layer’s tile can be only as big as to fit in this shared memory.
For ‘M’ output channels in intermediate layer:
SHRD = S2*M*4
‘SxS’ is the intermediate layer’s tile size
‘4’ to consider size of float.
‘M’ is the number of channels in intermediate layer.

## Slide 35: Layer Fusion – Analytical Model
Considering, kernel for both layers is of dimension [M][M][K][K]
where both input and output number of channels is equal for keeping the overall calculation simple.
For ‘SxS’ intermediate layer tile, we get:
Tile size of input layer: S+K-1
Tile size of output layer: S-K+1
Considering stride of ‘1’ and padding to input and output feature map dimensions same.
The input, intermediate & output feature map will be of ‘MxH’x’W’ dimension.

## Slide 36: Layer Fusion – Analytical Model
Thus number of computations
= No. of computation in a tile * number of tiles
No. of computation in a tile = K2C.M.S2
where K2C is the computation for a single convolution.
Same is done for ‘M’ number of channels.
And repeated for S2 times i.e. number of elements in a single channel of intermediate layer.

## Slide 37: Layer Fusion – Analytical Model
Number of tiles =
Where (s – K + 1) is the output layer tile size.
Therefore, number of computations =
Computation in traditional convolution = K2MCHW

## Slide 38: Layer Fusion – Analytical Model
Thus, number of re-computations =
As S>>K i.e. the intermediate tile size tends to be much higher than kernel size, the additional computation tends to 0.

## Slide 39: Layer Fusion for gradient update
We applied the same fusion approach to back propagation gradient update.
The time increases in NHWC fusion based approach since the convolution is across the output channel rather than input channel which is the lowest dimension.
Thus, we have non-unit strided access to memory.
Chart: BP Fused vs non-fused implementation
| W/O Fusion | With fusion
Layer 1 | 1.42 | 4.82
Layer 2 | 1.42 | 1.86

## Slide 40: Layer Fusion for BP – transpose weight matrix
The problem can be solved by taking a transpose of weight matrix.
The transpose kernel time comes to 7us which is <0.1% of the actual gradient update time.
We again see ~2x speed up of the fused layer over the non-fused version and ~18% speed up overall.
Chart: BP - Fused approach with weight transpose
| W/O Fusion | With fusion
Layer 1 | 1.42 | 1.62
Layer 2 | 1.42 | 0.619
Weight transpose | 0.007

## Slide 41: Multi-GPU DNN training
Neural networks grow deeper for accuracy
  e.g., Resnet-152, Inception-v3, Faster R-CNN
Large training dataset
  e.g., ImageNet
Single GPU takes several days/weeks to train the network []
Multi-GPU necessary to achieve faster training.

## Slide 42: Multi-GPU training - Challenge
Communication and synchronization
Data parallel approach chosen for distribution of data (features and network model) among multiple GPUs as CNNs are main focus of this project.
Evaluation platform:
  4 GTX 1080Ti connected to two NUMA nodes (2 GPUs/NUMA node)
  GPU0 -> GPU1 – P2P access enabled
  GPU0/1 -> GPU 2/3 – Resolves to normal memcpy procedure

## Slide 43: Multi-GPU training - Analysis
AlexNet chosen as evaluation platform as it contains most of the commonly used layers covering reasonable configuration ranges
Communication overhead on total training time vs Batch size
Increasing number of GPUs -> Increasing overhead; also involves communication between 2 NUMA nodes via SMP
Increasing batch size –> lower number of communication modules in an epoch
Chart: Multi-GPU communication
| 16 | 32 | 64 | 128
AlexNet - 2 GPUs | 0.02809 | 0.01909 | 0.011436 | 0.0084076
AlexNet - 4 GPUs | 0.058767 | 0.040666 | 0.023343 | 0.016987

## Slide 44: Multi-GPU training - Analysis
Convolutional layers – computation dominant; lower weight kernels
  e.g., Conv2:
  Weight_dim = ~72MB
  Number of operations = 896M operations
Fully connected layers – weight_dim/(no of computations) ratio high
  e.g., FC2:
  Weight_dim = ~67MB
  Number of operations = 33M operations
Chart: AlexNet - P2P communication
| Conv1 | Conv2 | Conv3 | Conv4 | Conv5 | FC1 | FC2 | FC3
Computation time | 53.2257 | 517.66 | 567.9732 | 326.5089 | 214.0671 | 129.0756 | 130.3554 | 1.5928
Communication time | 0.028288 | 0.80995 | 6.2874 | 1.7871 | 6.2853 | 48.582 | 83.0899 | 0.14263

## Slide 45: Multi-GPU training - Conclusions
Convolutional layer dominated by computation. Computation component scales better with newer architectures than communication component.
Communication component can be reduced by increasing the batch size.
Strong scaling -> Higher batch size affects accuracy for a given training problem for fixed number of epochs (or) needs more epochs
Intra-GPU hybrid approach for data split would result in enough GPU occupancy, allowing multi-GPU scaling with reasonable batch size.

## Slide 46: References
L. Song, J. Mao, Y. Zhuo, X. Qian, H. Li, and Y. Chen, “Hypar: Towards hybrid parallelism for deep learning accelerator array,” in 25th IEEE HPCA 2019, Washington, DC, USA , 2019.
Y. Lecun, L. Bottou, Y. Bengio, and P. Haffner, “Gradient-based learning applied to document recognition,” in Proceedings of the IEEE, pp. 2278–2324, 1998.
K. He, X. Zhang, S. Ren, and J. Sun, “Deep residual learning for image recognition,” in 2016 IEEE Conference on Computer Vision and Pattern Recognition, CVPR 2016, Las Vegas, NV, USA, June 27-30, 2016 , pp. 770–778, 2016
A. Krizhevsky, I. Sutskever, and G. E. Hinton, “Imagenet classification with deep convolutional neural networks,” in Advances in NIPS 25 , pp. 1097–1105, Curran Associates, Inc., 2012.
A. Krizhevsky, “Learning multiple layers of features from tiny images,” Technical report., 2009.
M. Alwani, H. Chen, M. Ferdman, and P. Milder, “Fused-layer CNN accelerators,” in 49th Annual IEEE/ACM International Symposium on Microarchitecture (MICRO) , 2016.
Lym, Sangkug, Armand Behroozi, Wei Wen, Ge Li, Yongkee Kwon, and Mattan Erez. "Mini-batch Serialization: CNN Training with Inter-layer Data Reuse." arXiv preprint arXiv:1810.00307 (2018).
Jung, Daejin, Wonkyung Jung, Sunjung Lee, Wonjong Rhee, and Jung Ho Ahn. "Restructuring Batch Normalization to Accelerate CNN Training." arXiv preprint arXiv:1807.01702(2018)
https://github.com/catchchaos/CUDA-CNN
Yadan, Omry, Keith Adams, Yaniv Taigman, and Marc'Aurelio Ranzato. "Multi-gpu training of convnets." arXiv preprint arXiv:1312.5853 (2013).